## Slide 1: Virtual Memory: Systems 15-213: Introduction to Computer Systems 16th Lecture, Oct. 19, 2010
Instructors:
Randy Bryant and Dave O’Hallaron

## Slide 2: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 3: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 4: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 5: Simple Memory System Page Table
Only show first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN

## Slide 6: Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set

## Slide 7: Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 8: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36

## Slide 9: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0
0x2E
2
0x0B
N
Y
TBD

## Slide 10: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 11: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 12: Single level page table
64bit address space, 4KB page size, 4GB physical memory
One entry per virtual page
  264 addressable bytes/212 bytes per page = 252 page table entries
Page table entry size
  One page table entry contains:
    Physical page number + Access control bits
  4GB physical memory = 232 bytes
    232 bytes memory / 212 bytes per page = 220 physical pages
    20 bits needed for physical page number
  Page table entry = ~ 4 bytes
Page table size
  252 page table entries * 4 bytes = 254 bytes (16 petabytes) per process

## Slide 13: Multilevel page table
Let’s make sure that any page table requires only a single page (4KB)
  Page table entry = ~ 4 bytes
  4KB page / 4bytes per PTE = 1024 entries
  10 bits of address space needed
  We have 52 bit address for page table
  We need ceiling(52/10) = 6 levels needed !
For each page table access, we need 6 memory accesses

## Slide 14: Inverted Page Table
We only have 4GB physical memory
  232 bytes memory / 212 bytes per page = 220 physical pages
If we only store a single page table entry per physical page
(table is indexed by PPN)
  Each page table entry has process ID, VPN, and access info
  16 bit process ID, 52bit VPN, 12 bit access info = 80 bits = 10 bytes
  220 PTE * 10 bytes = 10MB
For each (VPN, pid) pair, we need to find where it is in the page table by comparing it with all entries
  Linear time, up to 220 memory accesses……
Hashing to the rescue -> Hashed Inverted Page Tables

## Slide 15: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge

## Slide 16: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 17: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE

## Slide 18: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
CD: Caching disabled or enabled for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 1 PTEs only).
G: Global page (don’t evict from TLB on task switch)
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63

## Slide 19: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
CD: Cache disabled (1) or enabled (0)
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
G: Global page (don’t evict from TLB on task switch)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 20: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 21: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available next
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
36
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 22: Virtual Memory of a Linux Process
Kernel code and data
Memory mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%esp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x08048000 (32)
0x00400000 (64)
Different for each process

## Slide 23: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
vm_flags
vm_flags
vm_flags

## Slide 24: Linux Page Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a non-existing page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)

## Slide 25: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 26: Memory Mapping
VM areas initialized by associating them with disk objects.
  Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate a physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 27: Demand paging
Key point: no virtual pages are copied into physical memory until they are referenced!
  Known as demand paging
Crucial for time and space efficiency

## Slide 28: Sharing Revisited: Shared Objects
Process 1 maps the shared object.
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 29: Sharing Revisited: Shared Objects
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the shared object.
Notice how the virtual addresses can be different.

## Slide 30: Sharing Revisited: Private Copy-on-write (COW) Objects
Two processes mapping a private copy-on-write (COW) object.
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 31: Sharing Revisited: Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault.
Handler creates new R/W page.
Instruction restarts upon handler return.
Copying deferred as long as possible!
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 32: The fork Function Revisited
VM and memory mapping explain how fork provides private address space for each process.
To create virtual address for new new process
  Create exact copies of current mm_struct, vm_area_struct, and page tables.
  Flag each page in both processes as read-only
  Flag each vm_area_struct in both processes as private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new pages using COW mechanism.

## Slide 33: The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
  Programs and initialized data backed by object files.
  .bss and stack backed by anonymous files .
Set PC to entry point in .text
  Linux will fault in code and data pages as needed.
Memory mapped region
for shared libraries
Runtime heap (via malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
Private, demand-zero
libc.so
.data
.text
Shared, file-backed
Private, demand-zero
Private, demand-zero
Private, file-backed
a.out
.data
.text

## Slide 34: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
  start: may be 0 for “pick an address”
  prot: PROT_READ, PROT_WRITE, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)

## Slide 35: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 36: Using mmap to Copy Files
#include "csapp.h"
/*
* mmapcopy - uses mmap to copy
* file fd to stdout
*/
void mmapcopy(int fd, int size)
{
/* Ptr to mem-mapped VM area */
char *bufp;
bufp = Mmap(NULL, size,
PROT_READ,
MAP_PRIVATE, fd, 0);
Write(1, bufp, size);
return;
}
/* mmapcopy driver */
int main(int argc, char **argv)
{
struct stat stat;
int fd;
/* Check for required cmdline arg */
if (argc != 2) {
printf("usage: %s <filename>\n”,
argv[0]);
exit(0);
}
/* Copy the input arg to stdout */
fd = Open(argv[1], O_RDONLY, 0);
Fstat(fd, &stat);
mmapcopy(fd, stat.st_size);
exit(0);
}
Copying without transferring data to user space .